## Slide 1: 48V Systems - Power Inverter (Motor Control ECU)
Our Understanding
Experience
Strength
Design and Development of Power Inverter (Motor Control ECU) for
  48V Mild Electric Vehicle
  Functional Safety – ISO 26262 Compliance
AutoSAR Compliant Architecture
Validation and Testing – Dyno Testing
No of Resources
20+ Resources
2+ SMEs
Solutions / offerings
Integrated Power Inverter (Motor Control ECU)
High Performance Motor Control Algorithm
Model Based Development
Liquid Cooled Thermal Management
Safety Compliance – ISO 26262
EMI / EMC Compliance
Partner Eco System
Hardware Fabrication and Components Assembly
EMI / EMC Testing
Challenges
High Efficiency
Safety and Reliability
Thermal Management
Compact Design
Case Study
Design and Development of an Integrated Motor Control Unit for Interior Permanent Magnet Synchronous Motor for Mild Hybrid Electric Vehicle

## Slide 2: Case Study 1: 48V Power Inverter (Motor Control ECU) for HEV (1/6)
Objective:
Design and Development of an Integrated Motor Control Unit for Interior Permanent Magnet Synchronous Motor for Hybrid Electric Vehicle
Integrated ECU
Thermal Model
Dyno Testing
Safety Architecture
Control Processor
Monitor Processor
HW Protection Logic
MP Heart beat
PWM Enable
Phase cutoff
Initial
Phase cutoff Final
Phase current
Phase voltage
Motor, board temperature
PWM Final
PWM Initial
Driver Diagnostics
Motor position
CP Heart beat
Motor Driver
Motor
Phase cut off circuit
Motor Position
CAN
SPI
ENG2
ENG4
ENG5
ENG5
ENG6
ENG6
ENG7
ENG8
ENG9
ENG10
High Level Specifications:
System Voltage: 48V
Motor Capacity: 18 kW, 65 Nm, 18,000 RPM
Motor Type: IPMSM
For European Tier-1
48V 18kW 65Nm IPMSM for Mild HEV
Features:
Motor Control Algorithm: Sensored Vector Control : FOC
Inverter: Two Level Voltage Source Inverter: Full Bridge SiC based MOSFET
PWM Topology: Space Vector PWM
Model Based Development
Regenerative Braking Capability
Fault Management: Over Voltage, Over Current and Over Temperature etc.
Diagnostics and Network Management
Liquid Cooled Thermal Management
Scope:
End to End Product Development Include
System Level Design
Software Design and Development:
Hardware Design and Development
Testing: Software, Hardware, System and Dyno Testing
AutoSAR Compliance
Functional Safety Compliance : ISO 26262 – ASIL-C

## Slide 3: Case Study 1: Motor Control Algorithm Development Flow – Model Based Development (2/6)
Requirement Analysis
Design
Development
Testing
Evaluation
Space Vector & Sectors
FOC
Clark Transform
Park Transform
Inverse Park
Sector
Vu, Vv, Vw
Flux Response
Torque Response
SVPWM
MBD : Mat lab / Simulink / State flow
Auto code Generation: Target link

## Slide 4: Case Study 1: Hardware Development Workflow & Thermal Management of Power Inverter (3/6)
Define Architecture
Select Key Components
Schematic Design
PCB Layout
Assemble, Test & Debug
EMI/EMC Conformance Test
Hardware Design Tools:
Mentor Graphics,OrCAD,Simetrix, pSpice
Motor Controller ECU
Main Controller
Current Sensor
Capacitor
Power
Isolation
Hardware Development Workflow
Liquid Cooling based Thermal Management of Power Inverter had been done to study the temperature in MOSFET junctions and to control the liquid flow rate accordingly
Inputs for the modelling
- 3D Geometry of the model
- Boundary Conditions like inlet mass flow rates and Power
dissipation of MOSFETS
Thermal Modelling and Simulations were performed with the given Ambient conditions, MOSFET junction temperature and flow rate
SW Tools used :
Meshing & analysis: ICEM CFD & Fluent
Thermal Management of Power