## Slide 1
2018
48V MILD HYBRID EDS
ECU Development

## Slide 2: EDS Controller – Project Overview
Objective:
  48V mild hybrid system Motor controller design
Scope:
48 Volt mild hybrid control design (HW and SW).
Motor Traction control.
Regenerative charging
Start/Stop control
Hardware Development
Application SW Development
Platform SW Development
ISO26262 Compliant Functional Safety – ASIL C
2
Copyright © 2017 Tech Mahindra. All rights reserved.

## Slide 3
Two CPU system Architecture
3 Phase Mosfet motor Driver for Inverting DC-AC
60Nm /18KW/21000RPM PMSM closed loop control by FOC.
Torque control and Regenerative control
Start /Stop functionality
  Mechanical 3D Model Development
  PCB Placement, Routing and Gerber Release
  Traction motor is overheat protection
  Mosfet high temperatures protection
  Smoothing condenser high temperatures protection control
HW Overview
EDS Controller – HW Development Overview

## Slide 4
Functionalities – Torque-Boost, Generator Control, Start-Stop
Model Based Design for Application Software Development
    Field Oriented Control (FOC) of 3 Phase Multicoiled- PMSM Motor using PI control of Torque component of current (Iq) and Flux component of current (Id)
    Space Vector Pulse Width Modulation (SVPWM) used for 3 phase inverter
    Field Weaking Control
    Plant Model Development – Inverter Model, DQ Modeling, PMSM Motor Model, Load Model, Multi Coil
    Model In Loop (MIL), AutoCode Generation & Software In Loop (SIL)
    ISR Based Motor Control – Sampling Period 50 uS (20Khz)
    ISO26262 Compliant Monitor Processor Software Development
    Tools MATLAB-Simulink and TargetLink
Platform SW is developed using ARCCORE AutoSar Stacks
  BSW Stack Configuration, CDD Configuration, MCAL Configuration
  RTE Configuration
  Tools - EB-Tresos for MCAL, HighTec Compilers
SW Overview
EDS Controller – SW Development Overview
Field Oriented Control of PMSM Motor

## Slide 5
Requirements Specifications
EDS System Requirements
Software Requirements Specifications
Hardware Requirements Specifications
High Level Design
Modelling and Simulation
Algorithm and logic definition
Simulink model development
MIL testing
Auto coding and SIL testing
Data dictionary development
Auto coding
SIL testing
Integration testing
Support for Integration testing
EDS Parameter tuning
Maintenance
Bug fixes
Calibration change
Fine tuning the application
EDS SW Development – Model Based Design
Model Based Design – Application SW Development

## Slide 6: EDS Controller – Challenges
Challenges
Constraints on ECU size, dimensions – Divided into 5 PCBs – Current Sensor, Power Board, Cap Board, Digital Boards
Driver Circuits for Multi-Coil (3 phase divided into 12 coils) – PCB Lay-outing, Synchronism for driving MOSFETs
ADC Sampling for all 12 coils
FOC based control for Multi-Coil based PMSM Motor
Functional Safety using Monitor Processor – To be sync with Control Processor
6
Copyright © 2017 Tech Mahindra. All rights reserved.